## Slide 1: Final Research Report
William Skamser

## Slide 2: Research Project Goal and Approach
The goal of this project was to use GMAT (General Mission Analysis Tool) to validate low-thrust orbital trajectories.
Unfortunately, GMAT does not have a built-in method to solve low-thrust problems.
Approach was to use GMAT’s API to run scripts through an exterior optimization algorithm (SNOPT). And develop a tool to automate this process.

## Slide 3: Development of GMAT Low-Thrust Solving Function
Using GMAT’s Matlab API and SNOPT’s Matlab interface, a function was developed that was capable of propagating and optimizing low-thrust trajectories.
The function reads data from a setup Excel file and auto-generates a GMAT script to propagate low-thrust trajectories.
  Able to propagate any low-thrust trajectory.
The function can be prompted to optimize the trajectory to meet constraints or minimize the time of flight while meeting constraints.
  Can optimize any continuous, constant magnitude, low-thrust trajectory.

## Slide 4: How the function works
Reads initial guess and setup data from Excel file
Creates GMAT Script that can propagate Low-Thrust trajectory
Enter SNOPT optimization loop
  Uses the in-plane and out-of-plane thrust angles and time of flight as design variables
  Updates GMAT thrust trajectory file and rerun GMAT script
  Extract the satellite’s final state vector as constraint function
  Continue the loop until feasibility and optimality tolerance are achieved
Long run time due to saving files and rerunning GMAT script for every iteration

## Slide 5: Method to Reduce Optimization Run Time
Reducing number of steps
200 Steps
10 Steps
17 Minutes
16 Hours

## Slide 6: Method to Reduce Optimization Run Time
2) First optimize to meet constraints then optimize for time of flight
10 Steps
9 Minutes
8 Minutes
10 Steps

## Slide 7: Other Examples
Earth to Jupiter Solution
200 Steps
Earth to Mars Solution used in Conference Paper Link
300 Steps

## Slide 8: Potential to do flybys (with additional work to function)
Matlab Function already has an option for planetary force models
Would need a smaller step size in GMAT’s integrator
  Even longer run times